## Slide 1
UNBSJ Parking Digital Twin
CS 4555 Final Project · April 2026
UNBSJ
Parking Digital Twin
CS 4555 — Final Project Group A/B: Christian, Farbod, Miko, Obi

## Slide 2
System Overview
• A full-stack digital twin of all 16 UNBSJ parking lots, modelling and predicting parking demand and vacancy across campus in real time.
Core Pillars
• Real institutional data — scraped UNB course schedules, enrolment counts, residence data
• Behavioural modelling — attendance rates, commuter split, transportation modes, carpooling
• Hybrid prediction — Process-Based Model curves + Data-Driven residual correction layer (DDM)
• Real external data — 35,705 real parking observations imported from UCI Birmingham dataset
• Live guidance — 30-second visibility-aware polling, spot-level SVG mini-maps, personalised recommendations
What the system delivers
• Current occupancy view per lot and per individual spot
• Predictive occupancy forecasts for any future date/time
• Optimal lot + spot recommendation for a specific building or full class schedule
• What-If scenario explorer — campus-wide and personal schedule views
• Guest quick-recommend endpoint (no login required)
• Event-size modelling (small / medium / large campus events)
Deployed Stack
• Frontend → Vercel (React 18 + Vite + Tailwind)
• Backend → Fly.io (Node.js + Express + TypeORM)
• Database → Supabase PostgreSQL (prod) / SQLite (local)
• Maps → Google Earth Engine + GeoNB 2025 satellite imagery

## Slide 3
How It Works — High Level
1 Data Collection
• Student enrolment, residence data, course schedules scraped from UNB Self-Service API
• Staff population modelled from institutional data (650–950 estimated staff)
• Behavioural assumptions: attendance 75–85 %, solo-driver 75–85 %, carpool 5–15 %
2 Campus Presence Modelling
• 15-minute time slots: sum enrolled students in active classes + 1 instructor each
• Add non-teaching staff by time-of-day range
• Convert people → vehicles using attendance × commuter × solo/carpool split
• Output: pplOnCampusByTime.json — vehicles on campus (min / midpoint / max)
3 Prediction Engine
• Process-Based Model: per-lot-type occupancy curves × academic calendar period × day-of-week multiplier
• DDM residual layer: tanh-weighted correction from historical observations (weight = tanh(n/10))
• Campus parameters (carpool_rate, absence_rate, etc.) stored in DB and applied at runtime
4 Outputs
• Predicted occupancy % and free spots per lot
• Confidence level: live · data-backed · curve-estimate
• Best lot + specific spot recommendation (occupancy-aware spread selection)
• Day-profile charts and next-hour forecasts
• Personal what-if comparison (baseline vs event scenario)

## Slide 4
Database Schema — Core Tables
Parking System
• parking_lots — name, campus, capacity, imageUrl
• parking_spots — label, section, row, slotIndex, isAccessible, distanceToEntrance, parkingLotId
• parking_spot_readings — status (empty/occupied), recordedAt, parkingSpotId
Prediction & Analytics
• historical_proxy_data — sourceName (lot UUID), recordedAt, occupancyPct, metadata (period, eventSize, source)
• lot_occupancy_corrections — lotId, hour, dayOfWeek, period, meanResidual, nSamples
• campus_parameters — key, value, description (carpool_rate, absence_rate, effective_driver_rate, …)
User & Academic
• users — email, passwordHash, role, resident, disabled
• students — userId, studentId, year
• classes — classCode, startTime, endTime, building, enrolled, capacity, term
• class_schedule — studentId, classId, term, section
Spatial
• buildings — code, name, floors
• lot_building_distances — parkingLotId, buildingId, distanceMeters (192 manually mapped routes)
Key Design Patterns
• TypeORM entities define schema in TypeScript — type-safe, no raw SQL
• Zod schemas validate all incoming API payloads at runtime
• Composite PK on lot_occupancy_corrections (lotId, hour, dayOfWeek, period)

## Slide 5
Population Data & Behavioural Assumptions
Student Population
• Total: 2,319 (Undergraduate: 2,161 · Graduate: 158)
• Source: UNB Enrolment Data — Faculty Communication
• Residence: 300 (~12.9 %) | Commuter: 2,019 (~87.1 %)
• Source: UNB Residence Data — Faculty Communication
Student Assumptions
• Class attendance rate: 75–85 % (NSSE studies)
• Solo drivers: 75–85 %
• Carpool: 5–15 % (avg size 2.0–2.5 people/vehicle)
• Public transit: 5–10 %
Campus Parameters (stored in DB, runtime-applied)
• carpool_rate = 0.12
• non_driver_rate = 0.35
• effective_driver_rate = 0.53 (auto-derived)
• absence_rate = 0.15
• friday_absence_mult = 1.33 | monday_absence_mult = 1.13
Staff Population
• Estimated 650–950 total staff
• Derived from ~3,200 UNB-wide staff, scaled to UNBSJ's ~20–30 % student share
Staff Distribution
• Academic: 25–30 %
• Administrative: 30–35 %
• Support: 25–30 %
• Casual: 10–15 %
Work Mode
• On-site: 50–60 %
• Hybrid: 30–40 %
• Remote: 5–10 %
Demand Multiplier (per day-of-week)
• getDemandMultiplier(dow) =
effective_driver_rate × (1 − absence_rate × dow_mult)
• Applied to enrolment counts before normalising occupancy curve

## Slide 6
Hybrid Prediction Model — PBM + DDM
IMPLEMENTED
Process-Based Model (PBM) — always runs
• Per-lot-type occupancy curves: general, staff, resident, timed, phd
• Multiplied by academic calendar period (classes=1.0, exams=0.70, holiday=0.08, …)
• Multiplied by day-of-week demand multiplier from campus_parameters
• Weekend multipliers applied per lot type
• Event boost: none/small/medium/large × lot sensitivity × weekend bonus
• Enrollment activity index: 0.85 + 0.30 × activityIndex (when useEnrollment=true)
Confidence Levels
• data — ≥3 historical samples found for this lot/hour/dow/period
• curve — fell back to PBM curve (DDM residual still applied)
• live — real sensor reading within last polling cycle
Data-Driven Residual Layer (DDM) — hybrid correction
• Residuals stored in lot_occupancy_corrections keyed by (lotId, hour, dayOfWeek, period)
• Trust weight = tanh(nSamples / 10) — ramps from 0 → ~0.96 at 20 samples
• Final = curve + weight × meanResidual
Real Data Sources (35,705 records)
• UCI Parking Birmingham dataset (CC BY 4.0, Stolfi 2017)
• 30 NCP car parks, Oct–Dec 2016 → remapped to UNB fall 2024 calendar
• Round-robined to 6 UNB general lots by UUID
• 28,428 classes · 5,279 exams · 1,998 other period records
Residual Generation Scripts
• npm run gen-residuals — non-event corrections (15,744 slots updated)
• npm run gen-event-residuals — event/weekend corrections
Why Not Fully Data-Driven (yet)
• UNB-specific real sensor data not yet available
• Birmingham data provides real shape of demand; UNB calibration pending

## Slide 7
Walking Paths & Spatial System
The Problem
• Straight-line distance ignores sidewalks, construction zones, physical terrain
• GeneralParking1 → Oland Hall: 160 m straight line vs 207 m actual route
• Inaccurate distances break the entire recommendation engine
Our Solution
• 192 routes manually mapped by active UNBSJ students using Google Earth paths
• 16 parking lots × 12 buildings = every lot-to-building pairing covered
• Routes account for current campus construction, roads, and sidewalks
Spot-Level Distance
• recalc-distances script: parses spot labels (PREF-SECTION-NNN)
• distance = 8 + sectionIndex×10 + spotNumber×0.8, clamped [5, 80] m
• Stored in parking_spots.distanceToEntrance
lot_building_distances Table
• parkingLotId (UUID FK)
• buildingId (UUID FK)
• distanceMeters (float)
• Precomputed bridge table — O(1) lookup per lot-building pair
How Recommendations Use This
• Lot scored by: predictedFreeSpots × eligibility × distance to target building
• Spot selected within winning lot by distanceToEntrance to lot entrance
• walkMinutes returned to user = distanceMeters / 80 (m/min walking speed)
Occupancy-Aware Spot Spread
• < 30 % occupancy → random from nearest quartile (spread parkers out)
• ≥ 30 % occupancy → pure nearest-first (fill efficiently)
• Prevents clustering at entrance when lot is nearly empty

## Slide 8
Interactive Campus Map & Mini-Maps
Campus-Wide Map
• Base map: Google Earth Engine API for geospatial rendering
• High-res overlay: GeoNB 2025 Saint John satellite GeoTIFF, uploaded as GEE asset
• Custom GeoJSON polygons for all 16 lots, stored as GEE assets
• Map restricted to UNBSJ campus bounds (no free-scroll)
• Clicking a lot polygon opens that lot's mini-map view
• Live occupancy % shown per polygon via 30-second polling
Polling Architecture
• Visibility-aware: pauses when tab is hidden or device is offline
• Cancelled flag prevents stale updates after component unmount
• POLL_INTERVAL_MS = 30,000 (down from 5 s — reduces server load 6×)
SVG Mini-Maps (16 lots)
• Each lot has a custom SVG built in Figma from satellite imagery
• Exact real-world spot count, position, and angle per lot
• Spots organised into rows (A, B, C, …) with IDs like A-001, A-002
• Custom Figma export plugin required to preserve element IDs
Spot Status Colours
• Green — Available
• Red — Occupied
• Light Blue — Accessible (free)
• Dark Blue — Accessible (occupied)
Binding to Backend
• SVG rect id → ParkingSpot.label → ParkingSpot.id (UUID)
• seed.ts parses SVG for data-spot-label attributes to generate spots
• Real-time status updates recolour SVG rects via React state

## Slide 9
Course Data Collection & Campus Presence Model
Web Scraping — UNB Self-Service API
• Authenticated requests using token + session cookie from browser login
• Paginated requests retrieve all course sections per term
• Extracted: classCode, startTime, endTime, building, room, enrolled, capacity, term
• Output normalised to 24-hour HH:mm format, saved as scraped-courses.json
• Run once per semester via: npm run scrape-courses
Seeding into DB
• npm run seed-courses → populates classes and class_schedule tables
• Deduplicates on classCode + term to allow re-runs
Campus Presence Modelling
• For each 15-minute slot across the academic day:
Sum enrolled students in all active classes at that slot
Add 1 instructor per active class
Add non-teaching staff by time-of-day range
• Apply attendance rate × commuter ratio → commuter students present
• Apply solo/carpool split → vehicles
• Output: pplOnCampusByTime.json with carsOnCampusMidpoint per slot
activityCurve.service.ts
• computeGlobalActivityCurve(targetDate) fetches demand multiplier by dow
• Applies multiplier to enrolled count before normalising to 0–1 index
• Used by prediction engine as enrollmentActivityIndex

## Slide 10
Recommendation Engine
IMPLEMENTED
Parking Eligibility
• Each lot has eligibility rules: role, permit type, resident flag
• recommendBestParking(userId, buildingId, datetime, options) filters eligible lots
• Anonymous users fall back to DEFAULT_ANONYMOUS_PARKING_ELIGIBILITY (general lots only)
Lot Scoring
• Scored by: available spots, distance to target building, predicted occupancy
• predictOccupancy() called for each candidate lot at the target time
• Lots with < 1 predicted free spot are excluded
Spot Selection
• Empty spots sorted by distanceToEntrance ascending
• < 30 % lot occupancy → random from nearest quartile (spread mode)
• ≥ 30 % lot occupancy → nearest-first (fill mode)
Quick Recommend (Guest Access)
• GET /api/users/quick-recommend
• optionalAuth middleware — works with or without JWT
• Returns: lot, spot, distanceMeters, walkMinutes, occupancyPct, confidence
• Supports Live mode (current state) and Forecast mode (predicted)
• eventSize query param adjusts forecast for small/medium/large events
Personalised Day Plan
• GET /api/users/me/arrival-recommendation
• Fetches user's full class schedule for the day
• Groups classes by building, finds optimal lot per building cluster
• Returns ordered plan: arrive-at time, lot name, spot label, walk minutes
• Plan cached in Redis (5-min TTL) on prediction routes
Personal What-If
• GET /api/users/me/what-if-personal
• Runs recommendBestParking() twice: baseline (no event) vs scenario
• Returns side-by-side comparison with lotChanged and spotsDroppedBelow10 flags

## Slide 11
What-If Scenario Explorer
NOW IMPLEMENTED
Purpose
• Allows users to simulate how campus events or schedule changes affect parking
• Two independent tabs: Campus View and My Scenario
Campus View Tab
• Shows all 16 lots side-by-side: baseline vs event scenario
• Shared controls: date, time, event size (none/small/medium/large)
• Per-lot delta badges: occupancy change, free spots change
• Colour-coded occupancy bars (green → amber → red)
• Aggregated campus-wide summary: total spots affected
Scenario Controls (shared)
• Date picker, time picker, event size selector
• All lots re-predicted simultaneously on control change
My Scenario Tab
• Requires login — shows personalised impact based on user's actual schedule
• Calls GET /api/users/me/what-if-personal
• Side-by-side PersonalRecCard: baseline vs event scenario
• LotChanged warning banner when event pushes user to a different lot
• SpotsDroppedBelow10 warning when recommended lot becomes critically full
Backend Handler
• Fetches user's first building from schedule
• Calls recommendBestParking() twice (baseline + event) directly — no full plan re-run
• Returns lotChanged, spotsDroppedBelow10 comparison flags
Previous State
• Original presentation listed What-If as a 'Future Capability'
• Now fully implemented with both campus-wide and personalised views

## Slide 12
Key Scripts — Full Reference
Database Setup
• npm run seed — full DB init (lots, spots, buildings, distances)
• npm run seed-replace — rebuild parking tables, preserve users/courses
• npm run seed-courses — populate classes + class_schedule from JSON
Data Collection
• npm run scrape-courses — scrape UNB Self-Service API → scraped-courses.json
Historical Data
• npm run gen-historical — generate synthetic proxy records (Sep 2024–Apr 2026)
• npm run gen-historical-clear — clear table then regenerate
• npm run import-birmingham — download + import UCI Birmingham real data (35,705 records)
• npm run import-birmingham -- --clear — clear and reimport Birmingham data
Residual Corrections (DDM Layer)
• npm run gen-residuals — compute mean residuals for non-event records → lot_occupancy_corrections
• npm run gen-event-residuals — compute event/weekend residuals with prefixed period keys
Spot Attributes
• npm run populate-spots — fill isAccessible, spotType from SVG fill colours
• npm run recalc-distances — recompute distanceToEntrance from spot label parsing
Full Re-initialisation Order
1. npm run seed
2. npm run seed-courses
3. npm run populate-spots
4. npm run recalc-distances
5. npm run gen-historical
6. npm run import-birmingham
7. npm run gen-residuals
8. npm run gen-event-residuals

## Slide 13
System Architecture — 3-Tier
Tier 1 — Frontend (Vercel)
• React 18 + Vite + Tailwind CSS
• Automatic deploy on push to main branch
• Preview environments for feature branches
• Edge caching + static asset optimisation
• Mobile hamburger nav, responsive layout
• Visibility-aware 30-second polling (pauses when tab hidden)
Tier 2 — Backend (Fly.io)
• Node.js + Express + TypeScript
• Lightweight Fly Machines (shared-cpu-1x @ 1024 MB)
• Canadian region (YYZ) — low latency for UNBSJ users
• Scales horizontally; suspends when idle to reduce cost
• Request logging middleware — all calls logged to Fly dashboard
• Redis caching on prediction routes (5-min TTL, optional fallback)
Tier 3 — Database (Supabase / SQLite)
• Production: Supabase-hosted PostgreSQL
• Local development: SQLite via better-sqlite3
• APP_MODE env var switches between local and production paths
• TypeORM handles schema sync and all queries
External APIs
• Google Earth Engine — map rendering, lot polygon overlays
• GeoNB 2025 — high-resolution satellite imagery asset
• UNB Self-Service API — course schedule scraping (authenticated)
CI/CD
• GitHub → Vercel (frontend auto-deploy)
• GitHub → Fly.io (backend deploy via fly deploy)
CORS Policy
• Local mode: permissive cors() for development
• Production mode: origin-restricted to FRONTEND_ORIGIN env var

## Slide 14
Infrastructure — Vercel · Fly.io · Supabase
Vercel — Frontend Hosting
• Hosts React frontend with global CDN distribution
• Zero-config deployments — push to main → live in seconds
• Preview deployments for every PR — test before merging
• Edge caching reduces latency for users across Canada
Fly.io — Backend Hosting
• Runs Node.js inside lightweight Fly Machines (containers)
• Canadian region (YYZ) for UNBSJ proximity
• Auto-scales horizontally based on traffic
• Suspends machines during low traffic to minimise cost
• Health checks + automatic restarts ensure availability
• Built-in load balancing across instances
Supabase — Managed Database
• Cloud-hosted PostgreSQL for all production data
• Stores: parking, users, schedules, historical proxy data, residuals
• Dashboard for live table visualisation and SQL queries
• Identifies dead tables and misaligned relationships visually
• Eliminates need to manage database infrastructure
Environment Switching
• APP_MODE=local → better-sqlite3 (file-based, no network)
• APP_MODE=production → PostgreSQL via DATABASE_CONNECTION_STRING
• EARTH_ENGINE_CREDENTIALS_JSON → service account JSON from env
• EARTH_ENGINE_CLIENT_EMAIL + EARTH_ENGINE_PRIVATE_KEY → split-key fallback
• FRONTEND_ORIGIN → restricts CORS in production
• REDIS_URL → optional; caching degrades gracefully if absent

## Slide 15
Data Integrity — TypeORM + Zod
TypeORM — How Data Is Stored
• Schema defined in TypeScript entity classes — no raw SQL
• Decorators: @Entity, @Column, @PrimaryGeneratedColumn, @OneToMany, @ManyToOne
• Composite primary keys via @PrimaryColumn on bridge tables
• Relationships explicit and type-safe (e.g. ParkingLot → ParkingSpot[])
• synchronize: true in local mode auto-migrates schema changes
• Migrations used in production for controlled schema evolution
Key Entities
• ParkingLot, ParkingSpot, ParkingSpotLog (table: parking_spot_readings)
• HistoricalProxyData, LotOccupancyCorrection, CampusParameter
• User, Student, Course, ClassSchedule, Building, LotBuildingDistance
Zod — What Data Is Allowed In
• Runtime validation on all incoming API payloads
• Prevents malformed data reaching the database
• Single source of truth for expected request shapes
• Consistent error responses with field-level messages
Schemas in place
• createParkingLotSchema / updateParkingLotSchema
• recommendParkingSchema — buildingId, stateMode, predictedFreeSpots, predictedSpotStatuses
• createUserSchema / loginSchema / patchMeSchema
Together they provide
• End-to-end data integrity (TypeScript compile-time + Zod runtime)
• Safer database operations — no unvalidated writes
• Clear contracts between frontend ↔ backend ↔ database
Gap (known)
• Prediction controller currently uses manual parse helpers (parseEventSize, parseBool)
• Migrating to Zod schemas is a planned improvement

## Slide 16
Known Gaps & Planned Improvements
Missing — Campus Parameters Admin API
• campus_parameters table exists and is seeded on startup
• No routes registered — values only changeable via direct DB access
• Planned: GET /api/admin/campus-parameters + PATCH /api/admin/campus-parameters/:key
Missing — Prediction Route Zod Validation
• Prediction controller uses hand-rolled parseEventSize(), parseBool(), parseTermCodes()
• Inconsistent with rest of API which uses Zod schemas
• Error messages lack field-level detail
Missing — kml-to-edges Script
• Presentation references this as a key script for walking distance derivation
• Script no longer exists in codebase — distances already seeded but not reproducible
• Should be re-added or documented for future recalculation
Partial — Redis Plan Caching
• Redis IS implemented on prediction routes (5-min TTL)
• arrivalRecommendation.service.ts uses in-memory Map — not Redis
• Cross-request plan caching would reduce repeated expensive plan calculations
Data Limitation — Birmingham Transfer
• Birmingham data is UK commercial parking — not university-specific
• Business hours only (08:00–16:30); overnight residuals still synthetic
• DDM corrections will improve significantly once real UNB sensor data available
Lot Photos
• ResidentParking1/2, StaffParking3, TBD lots use placeholder images
• Requires physical campus visit to photograph actual lots
Future Enhancements
• Real UNB parking sensors → replace synthetic historical data
• Admin dashboard for campus parameters and lot management
• Push notifications when recommended lot fills up
• Semester-over-semester trend analysis using accumulated real data